## Slide 1: ECE 2001 Basic Circuit Theory
Lecture 2
Circuit Analysis Techniques

## Slide 2: An understanding of the operation and analysis of electronics is essential to an electrical engineer.
This lecture focuses on analyzing voltages and currents in a circuit.
This will be an application of KCL, KVL, and Ohm’s law.
It is also required to solve linear equations.
Notes: Example: applying basic laws (KCL, KVL, Ohm’s law) to directly solve a circuit

## Slide 3: Outline
Nodal analysis
  circuits w/o a voltage source
  circuits w/ a voltage source (supernode trick)
Mesh analysis
  Circuits w/o a current source
  Circuits w/ a current source (supermesh trick)
Nodal analysis versus Mesh analysis
Notes: Nodal analysis applies to any circuit; while mesh only to planar circuits. Computational circuit analysis using PSpice (Personal Simulation Program with Integrated Circuit Emphasis) also requires this fundamentals. See also the user forum: www.pspice.com

## Slide 4: Terminology

## Slide 5: Terminology Example
The nodes are a, b, c, d, e, f, and g. n=7.
Nodes b, c, e, and g are essential. ne=4.
The branches are v1, v2, R1, R2, R3, R4, R5, R6, R7, and I. b=10.
The essential branches are v1 - R1, R2 - R3, v2 - R4, R5, R6, R7, and I. be=7.
The meshes are v1 - R1 - R5 - R3 - R2, v2 - R2 - R3 - R6 - R4, R5 - R7 - R6, and R7 - I. l=4.
R1 - R5 - R6 is a path, but it is not a loop, nor an essential branch.
v1 - R1 - R5 - R6 - R4 - v2 is a loop but not a mesh. I - R5 - R6 is also a loop but not a mesh.
Remark: Alternatively, we may consider I - R5 - R6 a mesh and R5 - R7 - R6 not a mesh.
Why is that so?
Notes: Number of meshes: b-(n-1)=b_e-(n_e-1). The number of unknown is b_e (implying the number of independent equations is b_e); the number of independent KCL equations is n_e-1; the number of independent KVL equations is b_e-(n_e-1).

## Slide 6: Why study systematic methods for “not-so-simple” resistive circuits?
So far, we have analyzed relatively simple resistive circuits.
But as the circuits become more structurally complicated and involve more elements, applying the basic laws directly becomes cumbersome.
Two techniques will be introduced here:
  Nodal analysis (node-voltage method), which is based on Kirchhoff current law (KCL).
  Mesh analysis (mesh-current method), which is based on Kirchhoff voltage law (KVL).
Nodal analysis applies to any circuit; while mesh only to planar circuits.
These techniques give two systematic methods of describing the circuits with the minimum number of simultaneous equations.

## Slide 7: Nodal analysis in a nutshell: A simple problem
Problem: Find the voltages and currents in the circuit
Focus on voltage variables
Currents are expressed in terms of voltages (using Ohm’s law)
Use KCL at each node to form equations

## Slide 8: Nodal Analysis – 3 Basic Steps
Assign voltage variables to each node
Form equations: apply KCL at each node (with Ohm’s law)
Solve the resulting equations

## Slide 9: Nodal Analysis – 3 Basic Steps
Assign voltage variables to each node
Form equations: apply KCL at each node (with Ohm’s law)
Solve the resulting equations
Ohm’s law:
KCL:
(KCL at node 1)
(KCL at node 2)
Question: do we need to apply KCL at node 0?

## Slide 10: Nodal Analysis – 3 Basic Steps
Assign voltage variables to each node
Form equations: apply KCL at each node (with Ohm’s law)
Solve the resulting equations
If we express resistance as conductance, e.g., G1=1/R1,
we can write the equations in matrix form as
(This can be solved using techniques in linear algebra)

## Slide 11: Discussion on Step 1: node selection
Issue 1: Where to set the reference node?
Issue 2: Which nodes to pick for analysis? Do we pick nodes a, c, d, f?

## Slide 12: Discussion on Step 1: node selection
Issue 1: Where to set the reference node?
Issue 2: Which nodes to pick for analysis? Do we pick nodes a, c, d, f?
Reference node selection:
Select a node that can ease your computation
Common symbols for indicating a reference node, (a) common ground, (b) ground, (c) chassis ground.
Notes: Common ground and Ground both can be used to represent the real ground. (b) is more commonly used.

## Slide 13: Discussion on Step 1: node selection
Issue 1: Where to set the reference node?
Issue 2: Which nodes to pick for analysis? Do we pick nodes a, c, d, f?
Essential node: a point where three or more circuit elements join
Rule: We only need to select essential nodes!
Here, nodes b, c, e, and g are essential.
Q: How many variables?
Q: How many independent equations?

## Slide 14: Discussion on Step 2: Using KCL and Ohm’s law to form equations
Define the direction of the current at each branch
Be careful about the sign
Start of the arrow
End of the arrow
(Ohm’s law)
Notes: This is actually a restatement of Ohm’s law: when current flows through a resistor, voltage drops.

## Slide 15: Discussion on Step 2: What if there is a voltage source?
What is the problem with a voltage source?
  Ans: Cannot use Ohm’s law to determine the current (required by KCL)
Solutions
  Direct method: (i) form an equation using the voltage difference, and/or (ii) analyze a relevant and possibly inessential node (Usually, an additional variable needed)
  Supernode method: form a supernode and apply KCL on the supernode; then apply KVL (When you don’t want to introduce a new variable)

## Slide 16: Direct method: (i) form an equation using the voltage difference

## Slide 17: Supplementary on the direct method: analyze a relevant and possibly inessential node
5 V
3 Ω
a
Although node a is inessential (a node that connects only two circuit elements), adding node a to the nodal analysis helps:
One more variable va,
One more equation: v2 – va = 5

## Slide 18: More details on the supernode trick
Depending on what nodes the source is connected to, the approach varies.
Between the reference node and a non-reference mode:
  Set the voltage at the non-reference node to the voltage of the source
  In the example circuit :
Between two non-reference nodes
  The two nodes form a supernode.
  A supernode is formed by enclosing a (dependent or independent) voltage source connected between two non-reference nodes and any elements connected in parallel with it.

## Slide 19: More details on the supernode trick
Why Supernode?
  Nodal analysis requires applying KCL
  The current through the voltage source cannot be known in advance (Ohm’s law does not apply)
  By lumping the nodes together, the current balance can still be described
Note the following properties of a supernode:
  The voltage source inside the supernode provides a constraint equation needed to solve for the node voltages
  A supernode has no voltage of its own
  A supernode requires the application of both KCL and KVL
In order to apply KVL to the supernode in the example, the circuit is redrawn as shown.
Going around this loop in the clockwise direction gives:

## Slide 20: More details on the supernode trick
In the example circuit node 2 and 3 form a supernode
From Ohm’s Law:
Apply KCL at supernode:
Or this can be expressed as:

## Slide 21: More details on the direct method
Define branch currents
Apply KCL to nodes v2 and v3
Apply KCL to node v1 ,
Apply Ohm’s law to the branches
Constraints:
Thus arriving at the same 3 equations as before.
i6
i5

## Slide 22: * Discussion on Step 3: How to solve the equations in a more general way? – Cramer’s rule
In linear algebra,
where A is a matrix, b and x is a vector.
If A has non-zero determinant, then the theorem states that in this case the system has a unique solution, whose individual values for the unknowns are given by:
where Ai is the matrix formed by replacing the ith column of A by the column vector b.
=

## Slide 23: Example 1
Determine the nodal voltages
How many essential nodes?
Taking node 0 as the reference node, 3 unknown nodal voltages remain. There are also 4 unknown branch currents. Use Ohm’s law equations to replace the currents in the form of three nodal voltages, resulting in 3 equations.
Indicate unknowns

## Slide 24: Example 1
Unit of current in A and voltage in V.
At node 1:
At node 2:
At node 3:

## Slide 25: Example 1
Three equations with three unknowns v’s to solve:
Applying Cramer’s rule:
Similarly,

## Slide 26: Nodal analysis – with voltage source
When a voltage source is the only element between two essential nodes, the node-voltage method can be simplified.
In general, when you use the node-voltage method to solve circuits that have voltage sources connected directly between essential nodes, the number of unknown node voltages is reduced.
The reason is that, whenever a voltage source connects two essential nodes, it constrains the difference between the node voltages at these nodes to equal the voltage of the source.

## Slide 27: Summary of Nodal Analysis
The aim is to find the nodal voltages relative to that of a reference.
Given a circuit with n nodes, without voltage sources, the nodal analysis is accomplished via three steps:
  Select a convenient node as the reference node. Assign voltages v1,v2,…vn to the remaining n-1 nodes.
  Apply KCL to each of the n-1 non-reference nodes.
  Use Ohm’s law to express the branch currents in terms of node voltages.
  Solve the resulting n-1 simultaneous equations to obtain the unknown node voltages.
For the case of with voltage sources, a supernode method with KVL may be used (or via the direct method).

## Slide 28: Practice
(a) Use Nodal analysis to find the branch current through three resistors.
(b) Find the power associated with each source, and state whether the source is delivering or absorbing power.

## Slide 29: Practice
We can combine node 2 and 3 to form a Supernode
Apply KCL on the closed
boundary

## Slide 30: Practice
ne=4 essential nodes.
ne-1=3 nodal voltages v1, v2, and v3 as variables.
Voltage of node 1 is fixed.
Nodes 2 and 3 make up a supernode.
Variables: v2 and v3
Apply KCL to the supernode,
Constraints:

## Slide 31: Outline
Nodal analysis
  circuits w/o a voltage source
  circuits w/ a voltage source (supernode trick)
Mesh analysis
  Circuits w/o a current source
  Circuits w/ a current source (supermesh trick)
Nodal analysis versus Mesh analysis
Notes: Nodal analysis applies to any circuit; while mesh only to planar circuits. Computational circuit analysis using PSpice (Personal Simulation Program with Integrated Circuit Emphasis) will also be introduced here. See also the user forum: www.pspice.com

## Slide 32: What is a mesh?
A mesh is a loop that does not contain any other loop within it, where a loop is a closed path with no node passed more than once
This is a mesh and the current i1 is called mesh-current
This is NOT a mesh

## Slide 33: Mesh analysis only applies to planar circuits
A planar circuit is one that can be drawn in a plane with no branches crossing one another; otherwise it is nonplanar.
Example of a nonplanar circuit
The branch with the 13Ω resistor prevents the circuit from being drawn without crossing branches. Question: what if the diagonal 13 W resistor is removed?
Circuit (a) is a planar circuit because it can be equivalently drawn as (b), which has no cross branches

## Slide 34: Mesh analysis in a nutshell
Focus on current variables
Voltages are expressed using currents (Ohm’s law)
Use KVL for each mesh to form equations

## Slide 35: Basic Steps for Mesh Analysis
Assign mesh currents to each mesh
Apply KVL along each mesh loop
Solve the resulting equations

## Slide 36: Mesh currents are NOT branch currents
A mesh current is the current that exists only in the perimeter of a mesh; it may pass through many different branches.
Not always equal to a branch current.
May not be measurable, e.g. i2 (all elements in that mesh are shared)
I2
Note: Mesh current is just a virtual component. For example, the actual current I2 that flows in R2 equals to i2 - i4
Caution: KVL computes the actual voltage, which is computed using the actual current over the Ohm’s law.

## Slide 37: Mesh Analysis Example
Consider only essential nodes and branches, ne=2, be=3, l=be-(ne-1)=2.
The above circuit has two loops that are meshes (abefa and bcdeb).
The outer loop (abcdefa) is a loop, but not a mesh.
First, mesh currents i1 and i2 are assigned to the two meshes.
Applying KVL to the meshes:
Notes: Note: the outer loop is considered as a mesh from the mappable point of view.

## Slide 38: Mesh Analysis with Current Sources: Direct method and supermesh method
Same as the voltage source in Nodal Analysis, the presence of a current source makes the mesh analysis simpler in that it reduces the number of equations.
If the current source is located on only one mesh, the current for that mesh is defined by the source.
For example:
Here, the current i2 is equal to -5A

## Slide 39: Direct method
Same circuit as before.
Let the voltage on the 6 A current source be v
Apply KVL to meshes 1 and 2: note the sign of the common elements
Eliminating v:
Apply KCL to ground node:
Same two equations as using the supermesh case.
+
v
_

## Slide 40: Supermesh method (when I don’t want to introduce an additional variable)
Similar to the case of nodal analysis where a voltage source shared two non-reference nodes, current sources (dependent or independent) that are shared by more than one mesh need special treatment.
The voltage across a current source cannot be known in advance.
The two meshes must be joined together, resulting in a supermesh.
The supermesh is constructed by merging the two meshes and excluding the shared source and any elements in series with it.
A supermesh is required because mesh analysis uses KVL.
Intersecting supermeshes in a circuit must be combined to form a larger supermesh.

## Slide 41: Supermesh method with an example: Apply KVL over a supermesh loop
In this example, a 6A current course is shared between mesh 1 and 2.
The supermesh is formed by merging the two meshes.
The current source and the 2Ω resistor in series with it are also removed.

## Slide 42: Supermesh Example
Apply KVL to the supermesh
We next apply KCL to the node in the branch where the two meshes intersect.
Solving these two equations we get:
Note that the supermesh required using both KVL and KCL

## Slide 43: Practice
Use the mesh analysis to determine the power dissipated in the 4Ω resistor.

## Slide 44: Practice
Find the three mesh currents in the circuit.

## Slide 45: Practice

## Slide 46: Outline
Nodal analysis
  circuits w/o a voltage source
  circuits w/ a voltage source (supernode trick)
Mesh analysis
  Circuits w/o a current source
  Circuits w/ a current source (supermesh trick)
Nodal analysis versus Mesh analysis
Notes: Nodal analysis applies to any circuit; while mesh only to planar circuits. Computational circuit analysis using PSpice (Personal Simulation Program with Integrated Circuit Emphasis) will also be introduced here. See also the user forum: www.pspice.com

## Slide 47: Nodal analysis or mesh analysis

## Slide 48: Nodal vs Mesh Analysis
The greatest advantage of both methods is that they reduce the number of simultaneous equations that must be manipulated.
What then determines if one is going to be more efficient for solving a circuit problem?
There are two factors that dictate the better choice:
  The nature of the particular network
  The information required.

## Slide 49: Nodal vs Mesh Analysis
The nature of the particular network
  Suitable for mesh analysis:
  Suitable for nodal analysis:
The information required:
  node voltage or branch/mesh current wanted?
  For nonplanar networks, can only use nodal analysis, because mesh analysis only applies to planar networks.
Many series connected elements
Voltage sources
Supermeshes
A circuit with fewer meshes than nodes
Many parallel connected elements
Current sources
Supernodes
A circuit with fewer nodes than meshes

## Slide 50: Nodal Analysis by Inspection
There is a faster way to construct a matrix for solving a circuit by nodal analysis
Recall, for this circuit the nodal voltage can be solved as:
Therefore, in general, for a circuit that contains only independent current
sources with N non-reference nodes, the node-voltage equations may be written as:
Diagonal term Gkk is the sum of all conductance connecting to the kth node.
Off diagonal terms Gjk=Gkj are the negative sum of all conductance between the jth and kth node.
The sum of all independent current sources directly injecting to the kth node are denoted as ik. Current entering the node are treated as positive.
Unknown nodal voltages
(conceptually: flow out current = flow in current)

## Slide 51: Mesh Analysis by Inspection
Similarly, there is a faster way to construct a matrix for solving a circuit by mesh analysis
Recall, for this circuit the mesh current can be solved as:
Therefore, in general, for a circuit that contains only independent voltage sources with N non-reference nodes, the mesh-current equations may be written as:
Diagonal term Gkk is the sum of all sum of resistances in mesh k.
Off diagonal terms Rjk=Rkj are the negative sum of all resistances in common with the mesh j and k.
The sum taken clockwise of all voltage sources in mesh k are denoted as vk. Voltage rises are treated as positive.
Unknown mesh currents in clockwise direction
(conceptually: voltage drops = voltage rises)

## Slide 52: Expected learning outcome
Be able to apply the mesh analysis and nodal analysis along relevant tricks to find the voltages and currents in a circuit.